## Slide 1: Computer Vision w/ Raspberry Pi
Setting up a Raspberry Pi for image processing
Evan Hennis
Google Developer Expert in Machine Learning
@TheNurl
https://eckronsoftware.wordpress.com
https://github.com/ehennis
YouTube: Evan Hennis

## Slide 2: Bio
BS from Iowa State 2004
MS from Georgia Tech 2018
C# developer since 2004
GDE in Machine Learning 2019

## Slide 4
Fish Butler
Written this summer with my daughter (11) and my nephew (13)
https://play.google.com/store/apps/details?id=com.eckronsoftware.fishbutler

## Slide 5: Using Deep Learning to Predict Basketball Scores
https://www.manning.com/liveproject/using-deep-learning-to-predict-basketball-scores
$25 for early release and $50 normally

## Slide 6: Overview
Project Introduction
Raspberry Pi Setup (SD and OS)
Camera and API
TensorFlow v2 on ARM
MobileNetV2
Code and Demo
TensorFlow Lite Update
Future Projects
Conclusion

## Slide 7: Project Introduction
Raspberry Pi 3
Raspbian (Now Raspberry Pi OS)
Raspberry Pi Camera Module V2-8 Megapixel
Leigh Johnson (@grepLeigh)

## Slide 8: Raspberry Pi Setup (SD, OS, Camera)
SD Card
  >= 8GB
  Raspberry Pi Imager (I used Windows)
  Don’t:
    > 32GB
    Write protect your card
Raspberry Pi OS (Former Raspbian) or Noobs

## Slide 9: Camera and API
Camera: V2 8 Megapixel
API: PiCamera
  sudo apt install python3-picamera

## Slide 10: TensorFlow v2 on ARM
TensorFlow v2 doesn’t support ARM
TensorFlow Lite is preferred going forward
  I demonstrate the minimal changes to move toward TF Lite
TensorFlow 2 ARM WHL: https://github.com/lhelontra/tensorflow-on-arm/releases

## Slide 11: MobileNetV2
Built into Keras
  tensorflow.keras.application.mobilenet_v2
Version 3 is out

## Slide 12: Camera Code (Initialization)
Notes: Create the camera, set the resolution, set the frame rate (can increase with better hardware), create data container to hold the image, start the stream.

## Slide 13: Camera Code (Stream)
Notes: [Done in different thread] Grab the frame from the stream and clear the container

## Slide 14: Camera Code (Read)
Notes: Return the image data from the frame filled during the stream earlier

## Slide 15: MobileNet (Initialize)
Notes: Grab MobileNetV2 from the Keras library
Create the model from the keras collection. Setting the input variables. ‘imagenet’ is the trained weights

## Slide 16: MobileNet (Predict)
Notes: Convert frame to batch. Call preprocess_input from the Keras library. Predict the features. Call decode_predictions from the keras library.

## Slide 17: Main
Notes: Grab the frame from the camera class and pass to the prediction method

## Slide 18: Demo

## Slide 19: TensorFlow Lite
Convert Keras model to TF Lite Model
Install TensorFlow Lite subset
Create TF Lite Interpreter

## Slide 20: TensorFlow Lite (Model Conversion)

## Slide 21: TensorFlow Lite (Install)
Follow Guide: https://www.tensorflow.org/lite/guide/python
For the Raspberry Pi
  pip3 install https://dl.google.com/coral/python/tflite_runtime-2.1.0.post1-cp37-cp37m-linux_armv7l.whl

## Slide 22: TensorFlow Lite (TF Lite Interpreter)
Notes: Load the saved TF Lite model. Create the Interpreter. Load the input and output details. To predict, set the tensors and get the tensors.
NOTE: I am still using the preprocess_input and decode_predictions

## Slide 23: TensorFlow Lite (TF Lite Main)
Notes: Calls are all the same from the Main class

## Slide 24: Future Projects
Use transfer learning and train on a subset of images
  Family pictures, cars, etc.
Implement object tracking for security cameras
Add to an automated home to turn the lights on when you show up
Really dumb but someone online added a Pi to his clock so that if anyone was looking at the clock it would jump off the wall
Anything…

## Slide 25: Conclusion
Simple (Pretrained model, easy installs, and quick results)
Cheap ($35 Pi, $30 camera, $ SD card)
Easy (I was able to do it)

## Slide 26: Links
Leigh Johnson’s Project: https://towardsdatascience.com/portable-computer-vision-tensorflow-2-0-on-a-raspberry-pi-part-1-of-2-84e318798ce9
Camera Api: https://picamera.readthedocs.io/en/release-1.13/
TensorFlow 2 ARM WHL: https://github.com/lhelontra/tensorflow-on-arm/releases
MobileNetV2 Paper: https://arxiv.org/abs/1801.04381
MobileNet Classes: https://gist.github.com/yrevar/942d3a0ac09ec9e5eb3a
Code Repository: https://github.com/ehennis/Blog/tree/master/ImageDetection

## Slide 27: My Information
Twitter: @TheNurl
GitHub: https://github.com/ehennis
YouTube: Evan Hennis
Blog: http://blog.eckronsoftware.com
Email: EvanHennis@gmail.com
Manning liveProject: https://www.manning.com/liveproject/using-deep-learning-to-predict-basketball-scores